## Slide 1
UNIT -4 PART-1
INPUT/OUTPUT Management and Disk Scheduling

## Slide 2: Roadmap
I/O Devices
Organization of the I/O Function
I/O Buffering
Disk Scheduling
Raid
Notes: Memory management is a complex interrelationship between processor hardware and operating system software.
We focus first on the hardware aspect of virtual memory, looking at the use of paging, segmentation, and combined paging and segmentation.
Then we look at the issues involved in the design of a virtual memory facility in operating systems.

## Slide 3: Categories of I/O Devices
Difficult area of OS design
  Difficult to develop a consistent solution due to a wide variety of devices and applications
Three Categories:
  Human readable
  Machine readable
  Communications
(1) Human readable
Devices used to communicate with the user
Printers and terminals
  Video display
  Keyboard
  Mouse etc

## Slide 4: (3) Communication
(2) Machine readable
Used to communicate with electronic equipment like..
  Disk drives
  USB keys
  Sensors
  Controllers
  Actuators
Used to communicate with remote devices
  Digital line drivers
  Modems
Notes: Suitable for communicating with the computer user.
  Examples include printers and terminals, the latter consisting of video display, keyboard, and perhaps other devices such as a mouse.

## Slide 5
Differences in I/O Devices
Devices differ in a number of areas
  Data Rate
  Application
  Complexity of Control
  Unit of Transfer
  Data Representation
  Error Conditions
Notes: Suitable for communicating with remote devices.
  Examples are digital line drivers and modems.

## Slide 6: (1) Data Rate
May be massive difference between the data transfer rates of devices
Notes: There may be differences of several orders of magnitude between the data transfer rates.

## Slide 7: (2) Application
The use to which a device is put has an influence on the software and policies in the operating system and supporting utilities.
Examples:
  disk used for files requires the support of file management software.
  disk used as a backing store for pages in a virtual memory scheme depends on the use of virtual memory hardware and software.
These applications have an impact on disk scheduling algorithms.
Another example, a terminal may be used by an ordinary user or a system administrator.
  implying different privilege levels and perhaps different priorities in the operating system.

## Slide 8: (3) Complexity of control
A printer requires a relatively simple control interface.
A disk is much more complex.
This complexity is filtered to some extent by the complexity of the I/O module that controls the device.
(4) Unit of transfer
Data may be transferred as
  a stream of bytes or characters (e.g., terminal I/O)
  or in larger blocks (e.g., disk I/O).
Notes: A printer requires a relatively simple control interface while a disk is much more complex.
This complexity is filtered to some extent by the complexity of the I/O module that controls the device.

## Slide 9: (5) Data representation
Different data encoding schemes are used by different devices,
  including differences in character code and parity conventions.
(6) Error Conditions
The nature of errors differ widely from one device to another.
Aspects include:
  the way in which they are reported,
  their consequences,
  the available range of responses

## Slide 10: Roadmap
I/O Devices
Organization of the I/O Function
I/O Buffering
Disk Scheduling
Raid
Notes: Memory management is a complex interrelationship between processor hardware and operating system software.
We focus first on the hardware aspect of virtual memory, looking at the use of paging, segmentation, and combined paging and segmentation.
Then we look at the issues involved in the design of a virtual memory facility in operating systems.

## Slide 11: Techniques for performing I/O
Following summarized three techniques for performing I/O:
Programmed I/O:-
  The processor issues an I/O command, on behalf of a process, to an I/O module;
Interrupt-driven I/O:-
  The processor issues an I/O command on behalf of a process.
  If the I/O instruction from the process is nonblocking, then the processor continues to execute instructions from the process that issued the I/O command.
  Else the next instruction that the processor executes is from the OS, which will put
  the current process in a blocked state and schedule another process.
Q-1: List and briefly define three techniques for performing I/O.
Notes: From section 1.7
Programmed I/O:
  Processor issues an I/O command, on behalf of a process, to an I/O module;
  that process then busy waits for the operation to be completed before proceeding.
Interrupt-driven I/O:
  Processor issues an I/O command on behalf of a process.
  If the I/O instruction from the process is nonblocking, then the processor continues to execute instructions from the process that issued the I/O command.
  If the I/O instruction is blocking, then the next instruction that the processor executes is from the OS, which will put the current process in a blocked state and schedule another process.
Direct memory access (DMA):
  A DMA module controls the exchange of data between main memory and an I/O module.
  The processor sends a request for the transfer of a block of data to the DMA module and is interrupted only after the entire block has been transferred.
Table 11.1 indicates the relationship among these three techniques.

## Slide 12
Direct memory access (DMA):-
  A DMA module controls the exchange of data between main memory and an I/O module.
  The processor sends a request for the transfer of a block of data to the DMA module and is interrupted only after the entire block has been transferred.
Techniques for performing I/O

## Slide 13: Techniques for performing I/O
Table 11.1 indicates the relationship among these three techniques

## Slide 14: Evolution of the I/O Function
As computer systems have evolved, there has been a pattern of increasing complexity
and sophistication of individual components.
The evolutionary steps can be summarized as follows:
Processor directly controls a peripheral device
Controller or I/O module is added
  Processor uses programmed I/O without interrupts
  Processor does not need to handle details of external devices
3. Now interrupts are employed.
  The processor need not spend time waiting for an I/O operation to be performed, thus increasing efficiency.

## Slide 15
4. The I/O module is given direct control of memory via DMA.
  It can now move a block of data to or from memory without involving the processor, except at the beginning and end of the transfer.
I/O module is a separate processor
  CPU directs the I/O processor to execute an I/O program in main memory.
I/O processor
  I/O module has its own local memory
  Commonly used to control communications with interactive terminals
Evolution of the I/O Function

## Slide 16: Basic Operation Of DMA
When the processor wishes read or send a block of data, it issues a command to the DMA module by sending some information to DMA module. The information includes:
read or write command, sending through read and write control lines.
number of words to be read or written, communicated on the data lines and stored in the data count register.

## Slide 17
starting location in memory to read from or write to, communicated on data lines and stored in the address register.
address of the I/O device involved, communicated on the data lines.
After the information are sent, the processor continues with other work.
The DMA module then transfers the entire block of data directly to or from memory without going through the processor. When the transfer is complete, the DMA module sends an interrupt signal to the processor to inform that it has finish using the system bus.
Direct Memory Access

## Slide 18: DMA Configurations: 1. Single Bus
Some possibilities are shown here In the first example, all modules share the same system bus.
  The DMA module, uses programmed I/O to exchange data between memory and an I/O module through the DMA module.
  This is clearly inefficient: As with processor-controlled programmed I/O, each transfer of a word consumes two bus cycles (transfer request followed by transfer).

## Slide 19: DMA Configurations: 2.Integrated DMA & I/O
The number of required bus cycles can be cut substantially by integrating the DMA and I/O functions.
This means that there is a path between the DMA module and one or more I/O modules that does not include the system bus.
The DMA logic may actually be a part of an I/O module, or it may be a separate module that controls one or more I/O modules.

## Slide 20: DMA Configurations: 3. I/O Bus
This concept can be taken one step further by connecting I/O modules to the DMA module using an I/O bus
This reduces the number of I/O interfaces in the DMA module to one and provides for an easily expandable configuration.
In all of these cases the system bus that the DMA module shares with the processor and main memory is used by the DMA module only to exchange data with memory and to exchange control signals with the processor.
The exchange of data between the DMA and I/O modules takes place off the system bus.
Notes: This concept can be taken one step further by connecting I/O modules to the DMA module using an I/O bus
This reduces the number of I/O interfaces in the DMA module to one and provides for an easily expandable configuration.
In all of these cases the system bus that the DMA module shares with the processor and main memory is used by the DMA module only to exchange data with memory and to exchange control signals with the processor.
The exchange of data between the DMA and I/O modules takes place off the system bus.

## Slide 21: Summary flows of using DMA by processor
Issue command to DMA module, by sending necessary information to DMA module.
Processor does other work.
DMA acquire control on the system, and transfers data to and from within memory and external device.
DMA sends a signal to processor when the transfer is complete, system control is return to processor.

## Slide 22: Advantages
Allows a peripheral device to read from/write to memory without going through the CPU
Allows for faster processing since the processor can be working on something else while the peripheral can be populating memory
Disadvantages
requires a DMA controller to carry out the operation, which increases the cost of the system
cache coherence problems

## Slide 23: Roadmap
I/O Devices
Organization of the I/O Function
I/O Buffering
Disk Scheduling
Raid
Disk Cache
Notes: Memory management is a complex interrelationship between processor hardware and operating system software.
We focus first on the hardware aspect of virtual memory, looking at the use of paging, segmentation, and combined paging and segmentation.
Then we look at the issues involved in the design of a virtual memory facility in operating systems.

## Slide 24: I/O Buffering
Processes must wait for I/O to complete before proceeding
  To avoid deadlock certain pages must remain in main memory during I/O
It may be more efficient to perform input transfers in advance of requests being made and to perform output transfers some time after the request is made. This technique is known as buffering.
Block-oriented Buffering
Information is stored in fixed sized blocks
Transfers are made a block at a time
  Can reference data by block number
Used for disks and USB keys
Notes: To avoid deadlock, the user memory involved in the I/O operation must be locked in main memory immediately before the I/O request is issued, even though the I/O operation is queued and may not be executed for some time.
  If a block is being transferred from a user process area directly to an I/O module, then the process is blocked during the transfer and the process may not be swapped out.
To avoid these overheads and inefficiencies, it is sometimes convenient to perform input transfers in advance of requests being made and to perform output transfers some time after the request is made.

## Slide 25: Stream-Oriented Buffering
Transfer information as a stream of bytes
Used for terminals, printers, communication ports, mouse and other pointing devices, and most other devices that are not secondary storage
No Buffer
Without a buffer, the OS directly access the device as and when it needs

## Slide 26: Single Buffer
Operating system assigns a buffer in main memory for an I/O request
Block Oriented Single Buffer
For block-oriented devices,
  Input transfers are made to the system buffer.
  When the transfer is complete, the process moves the block into user space and immediately requests another block.
Called reading ahead, or anticipated input;
  it is done in the expectation that the block will eventually be needed.
Often this is a reasonable assumption most of the time because data are usually accessed sequentially.
  Only at the end of a sequence of processing will a block be read in unnecessarily.
Notes: When a user process issues an I/O request, the operating system assigns a buffer in the system portion of main memory to the operation.

## Slide 27: Stream-oriented Single Buffer
The single buffering scheme can be used in a line-at-a-time fashion or a byte-at-a-time fashion.
  Line-at-a-time operation is appropriate for scroll-mode terminals (sometimes called dumb terminals).
  Byte-at-a-time operation is used on where each keystroke is significant, or for peripherals such as sensors and controllers.
Notes: The single buLine-atffering scheme can be used in a line-at-a-time fashion or a byte-at-a-time fashion.
  -a-time operation is appropriate for scroll-mode terminals (sometimes called dumb terminals).
  Byte-at-a-time operation is used on where each keystroke is significant, or for peripherals such as sensors and controllers.

## Slide 28: Double Buffer
Use two system buffers instead of one
A process can transfer data to or from one buffer while the operating system empties or fills the other buffer
Notes: A process transfers data to (or from) one buffer while the operating system empties (or fills) the other.

## Slide 29: Circular Buffer
More than two buffers are used
Each individual buffer is one unit in a circular buffer
Used when I/O operation must keep up with process
Notes: Double buffering may be inadequate if the process performs rapid bursts of I/O.
The problem can often be alleviated by using more than two buffers.
When more than two buffers are used, the collection of buffers is itself referred to as a circular buffer with each individual buffer being one
unit in the circular buffer.

## Slide 30: Buffer Limitations
Buffering is a technique that smoothes out peaks in I/O demand.
However, no amount of buffering will allow an I/O device to keep pace with
a process indefinitely when the average demand of the process is greater
than the I/O device can service.
  Even with multiple buffers, all of the buffers will eventually fill up and
  the process will have to wait after processing each chunk of data.
However, in a multiprogramming environment, when there is a variety of
I/O activity and a variety of process activity to service, buffering is one tool
that can increase the efficiency of the operating system and the
performance of individual processes.

## Slide 31: Roadmap
I/O Devices
Organization of the I/O Function
I/O Buffering
Disk Scheduling
Raid
Notes: Memory management is a complex interrelationship between processor hardware and operating system software.
We focus first on the hardware aspect of virtual memory, looking at the use of paging, segmentation, and combined paging and segmentation.
Then we look at the issues involved in the design of a virtual memory facility in operating systems.

## Slide 32: Disk Performance Parameters
When the disk drive is operating, the disk is rotating at constant speed.
To read or write, the head must be positioned at the desired track and at the beginning of the desired sector on that track.
Track selection involves moving the head in a movable head system or electronically selecting one head on a fixed-head system.
Q-2: Briefly define the disk scheduling policies with example.

## Slide 33
Access Time = (SEEK TIME + ROTATIONAL DELAY)
Seek time:-
  On a movable-head system, the time it takes to position the head at the
  track is Known as seek time.
Rotational delay or rotational latency:-
  The time its takes for the beginning of the sector to reach the head is known as rotational delay.
Seek time + rotational delay = access time,
                The time it takes to get into position to read or
                write.
Transfer Time:-
Once the head is in position then the time taken to transfer the data is transfer time.
Disk Performance Parameters

## Slide 34: Disk Performance Parameters
The actual details of disk I/O operation depend on many things
  A general timing diagram of disk I/O transfer is shown here.
Notes: The actual details of disk I/O operation depend on the computer system, the operating system, and the nature of the I/O channel and disk controller hardware.
A general timing diagram of disk I/O transfer is shown in Figure 11.6.

## Slide 35: Disk Scheduling Policies
To compare various schemes, consider a disk head is initially located at track 100.
  assume a disk with 200 tracks and that the disk request queue has random requests in it.
The requested tracks, in the order received by the disk scheduler, are
  55, 58, 39, 18, 90, 160, 150, 38, 184.
RANDOM SHCHEDULING:-
  If we selected items from the queue in random order, then we can expect
  that the tracks to be visited will occur randomly, giving poor
  performance.
  This is called random scheduling

## Slide 36: First-in, first-out (FIFO)
The simplest form of scheduling is first-in-first-out (FIFO) scheduling, which processes items from the queue in sequential order.
This strategy has the advantage of being fair, because every request is honored in the order received.
With FIFO, if there are only a few processes that require access and if many of the requests are to clustered file sectors, then we can hope for good performance.
  However, this technique will often approximate random scheduling in performance, if there are many processes competing for the disk
  TRACKS:- 55, 58, 39, 18, 90, 160, 150, 38, 184.
Notes: Movie icon jumps to animation at http://gaia.ecs.csus.edu/%7ezhangd/oscal/DiskApplet.html
The simplest form of scheduling is first-in-first-out (FIFO) scheduling, which processes items from the queue in sequential order.
This strategy has the advantage of being fair, because every request is honored and the requests are honored in the order received.
This figure illustrates the disk arm movement with FIFO.
  This graph is generated directly from the data in Table 11.2a.
As can be seen, the disk accesses are in the same order as the requests were originally received.
With FIFO, if there are only a few processes that require access and if many of the requests are to clustered file sectors, then we can hope for good performance.
  But, this technique will often approximate random scheduling in performance, if there are many processes competing for the disk.

## Slide 37: FIFO - PERFORMANCE
Figure 11.7a illustrates
the disk arm movement
with FIFO.
  This graph is
  generated directly
  from the data in
  Table 11.2a

## Slide 38: Shortest Service Time First
The SSTF policy is to select the disk I/O request that requires the least movement of the disk arm from its current position.
Always choose the minimum seek time.
  TRACKS:- 55, 58, 39, 18, 90, 160, 150, 38, 184.
Notes: Select the disk I/O request that requires the least movement of the disk arm from its current position.
Thus, we always choose to incur the minimum seek time.
  Always choosing the minimum seek time does not guarantee that the average seek time over a number of arm movements will be minimum.
  However, this should provide better performance than FIFO.
Because the arm can move in two directions, a random tie-breaking algorithm may be used to resolve cases of equal distances.

## Slide 39: Shortest Service Time First
Always choosing the minimum seek
time does not guarantee that the
average seek time over a number of
arm movements will be minimum.
However, this should provide better
performance than FIFO.
Because the arm can move in two
directions, a random tie-breaking
algorithm may be used to resolve
cases of equal distances.

## Slide 40: SCAN
Arm moves in one direction only, satisfying all outstanding requests until it reaches the last track in that direction then the direction is reversed
  TRACKS:- 55, 58, 39, 18, 90, 160, 150, 38, 184.
Notes: With SCAN, the arm is required to move in one direction only, satisfying all outstanding requests en route, until it reaches the last track in that direction or until there are no more requests in that direction.
  The service direction is then reversed and the scan proceeds in the opposite direction, again picking up all requests in order.
This latter refinement is sometimes referred to as the LOOK policy.
The SCAN policy favors jobs whose requests are for tracks nearest to both innermost and outermost tracks and favors the latest-arriving jobs.

## Slide 41: SCAN
The arm is required to move in one
direction only until there are no
more requests in that direction.
The service direction is then
reversed and the scan proceeds in
the opposite direction, again picking
up all requests in order.
This latter refinement is sometimes referred to as the LOOK policy.
The SCAN policy favors jobs whose requests are for tracks nearest to both innermost and outermost tracks and favors the latest-arriving jobs.

## Slide 42: C-SCAN
The C-SCAN (circular SCAN) policy restricts scanning to one direction only.
  Thus, when the last track has been visited in one direction, the arm is returned to the opposite end of the disk and the scan begins again.
This reduces the maximum delay experienced by new requests.
  TRACKS:- 55, 58, 39, 18, 90, 160, 150, 38, 184.
Notes: The C-SCAN (circular SCAN) policy restricts scanning to one direction only.
  Thus, when the last track has been visited in one direction, the arm is returned to the opposite end of the disk and the scan begins again.
This reduces the maximum delay experienced by new requests.

## Slide 43: C-SCAN

## Slide 44: Performance Compared
Notes: T

## Slide 45: N-step-SCAN
The N-step-SCAN policy segments the disk request queue into sub queues of length N.
Subqueues are processed one at a time, using SCAN.
While a queue is being processed, new requests must be added to some
other queue.
If fewer than N requests are available at the end of a scan, then all of
them are processed with the next scan.

## Slide 46: FSCAN
Two sub queues
When a scan begins, all of the requests are in one of the queues, with the other empty.
All new requests are put into the other queue.
  Service of new requests is deferred until all of the old requests have been processed.
Notes: FSCAN is a policy that uses two subqueues.
When a scan begins, all of the requests are in one of the queues, with the other empty.
During the scan, all new requests are put into the other queue.
  Thus, service of new requests is deferred until all of the old requests have been processed.

## Slide 47: Disk Scheduling Algorithms

## Slide 48: Roadmap
I/O Devices
Organization of the I/O Function
I/O Buffering
Disk Scheduling
Raid
Notes: Memory management is a complex interrelationship between processor hardware and operating system software.
We focus first on the hardware aspect of virtual memory, looking at the use of paging, segmentation, and combined paging and segmentation.
Then we look at the issues involved in the design of a virtual memory facility in operating systems.

## Slide 49: RAID
Redundant Array of Independent Disks
The RAID scheme consists of seven levels, zero through six.
These levels do not imply a hierarchical relationship but designate different design architectures that share three common characteristics:
  1. RAID is a set of physical disk drives viewed by the operating system as a single logical drive.
  2. Data are distributed across the physical drives of an array in a scheme known as striping, described subsequently.
  3. Redundant disk capacity is used to store parity information, which guarantees data recoverability in case of a disk failure.
Q-3: Briefly define the seven RAID levels.
Notes: Movie icon links to animation at: http://gaia.ecs.csus.edu/%7ezhangd/oscal/RAIDFiles/RAID.htm
The RAID scheme consists of seven levels, zero through six.
These levels do not imply a hierarchical relationship but designate different design architectures that share three common characteristics:
  1. RAID is a set of physical disk drives viewed by the operating system as a single logical drive.
  2. Data are distributed across the physical drives of an array in a scheme known as striping, described subsequently.
  3. Redundant disk capacity is used to store parity information, which guarantees data recoverability in case of a disk failure.

## Slide 50
RAID
Parity data is used by some RAID levels to achieve redundancy. using XOR function to reconstruct the missing data.
For example, suppose two drives in a three-drive RAID 51 array contained the following data:
Drive 1: 01101101 Drive 2: 11010100
To calculate parity data for the two drives, an XOR is performed on their data:
01101101 XOR 11010100
10111001
The resulting parity data, 10111001, is then stored on Drive 3.
If Drive 2 were to fail, its data could be rebuilt using the XOR results of the contents of the two remaining drives, Drive 1 and Drive 3:
Drive 1: 01101101 Drive 3: 10111001 as follows:
10111001 XOR 01101101 11010100
The result of that XOR calculation yields Drive 2's contents. 11010100 is then stored on Drive 2, fully repairing the array.
In the case of a RAID 3 array of 12 drives, 11 drives participate in the XOR calculation shown above and yield a value that is then stored on the dedicated parity drive.

## Slide 51: RAID 0 - Stripped
RAID level 0 is not a true member of the RAID family, because it does not include redundancy.
The advantage of this layout is that if a single I/O request consists of multiple logically contiguous strips, then up to n strips for that request can be handled in parallel, greatly reducing the I/O transfer time.
Notes: RAID level 0 is not a true member of the RAID family, because it does not include redundancy.
The advantage of this layout is that if a single I/O request consists of multiple logically contiguous strips, then up to n strips for that request can be handled in parallel, greatly reducing the I/O transfer time.

## Slide 52: RAID 1 - Mirrored
Each logical strip is mapped to two separate physical disks so that every disk in the array has a
mirror disk that contains the same data.
A read request can be serviced by either of the two disks that contains the requested data,
whichever one involves the minimum seek time plus rotational latency.
A write request requires that both corresponding strips be updated, but this can be done in
parallel.
  Thus, the write performance is dictated by the slower of the two writes
Recovery from a failure is simple.
  When a drive fails, the data may still be accessed from the second drive.

## Slide 53: RAID 2 (Using Hamming code)
In a parallel access array, all member disks participate in the execution of every I/O
request.
Typically, the spindles of the individual drives are synchronized so that each disk
head is in the same position on each disk at any given time.
As in the other RAID schemes, data striping is used.
In the case of RAID 2 and 3, the strips are very small, often as small as a single byte or
word.
With RAID 2, an error-correcting code is calculated across corresponding bits on each
data disk, and the bits of the code are stored in the corresponding bit positions on
multiple parity disks.
Typically, a Hamming code is used, which is able to correct single-bit errors and detect
double-bit errors.

## Slide 54: RAID 3 bit-interleaved parity
RAID 3 is organized in a similar fashion to RAID 2.
The difference is that RAID 3 requires only a single redundant disk, no matter how large the disk array.
RAID 3 employs parallel access, with data distributed in small strips.
  Instead of an error-correcting code, a simple parity bit is computed for the set of individual bits in the same position on all of the data disks.
Notes: RAID 3 is organized in a similar fashion to RAID 2.
The difference is that RAID 3 requires only a single redundant disk, no matter how large the disk array.
RAID 3 employs parallel access, with data distributed in small strips.
  Instead of an error-correcting code, a simple parity bit is computed for the set of individual bits in the same position on all of the data disks.

## Slide 55: RAID 4 Block-level parity
A bit-by-bit parity strip is calculated across corresponding strips on each data disk
The parity bits are stored in the corresponding strip on the parity disk.
Notes: A bit-by-bit parity strip is calculated across corresponding strips on each data disk,
  and the parity bits are stored in the corresponding strip on the parity disk.

## Slide 56: RAID 5 Block-level Distributed parity
RAID 5 is organized in a similar fashion to RAID 4.
RAID 5 distributes the parity strips across all disks.
  A typical allocation is a round-robin scheme
  For an n-disk array, the parity strip is on a different disk for the first n stripes, and the pattern then repeats.
The distribution of parity strips across all drives avoids the potential I/O bottleneck of the single parity disk found in RAID 4.

## Slide 57: RAID 6 Dual Redundancy
Two different parity calculations are carried out and stored in separate blocks on different disks.
  Thus, a RAID 6 array whose user data require N disks consists of N+2 disks.
P and Q are two different data check algorithms.
  One of the two is the exclusive-OR calculation used in RAID 4 and 5.
  The other is an independent data check algorithm.
This makes it possible to regenerate data even if two disks containing user data fail.